## Slide 1: The Multi-Service IP Network for Railways
Felix Gerdes
Business Development Rail Transport & Mass Transit, EMEA
International IRSTE & IRSE Convention, New Delhi, 28 April 2012

## Slide 2: Agenda
The Opportunity for Further Progress
Coming: The Cost Avalanche
IP for Trackside Comms: Achieving Reliability
The Cisco Connected Signalling Architecture

## Slide 3: A Way Forward
Look Familiar?
Remove Technology Barriers
Adapt the Business
Achieve Growth, Prosperity
Example: Reliable, high capacity data and voice networks from the US to India gave birth to the BPO industry.
From The World is Flat, Thomas L. Friedman

## Slide 4: Implication of Mega Corridors in India
8 Mega Corridors by 2021
  Delhi – Mumbai Industrial Corridor: 204m
  Mumbai – Ahmedabad Corridor: 58m
  Bangalore – Belgaum: 38m
Source: Frost & Sullivan, Mega Trends in India: Macro to Micro Implications of Top MegaTrends in India to 2020, Sarwant Singh, Archana Amarnath, 02 Feb 2012
Commuter & Freight Rail Transport Growth will be Imminent

## Slide 5: A Possible Way Forward
RailTel: a service provider for Indian Railways, local government and businesses across India ...
RailTel rolls out ETCS Level 2
RailTel delivers train control comms as a another service

## Slide 6: Challenges Facing Railway Managers
Increasing Focus on the Customer
More Competition (Inter- and Intramodal)
How to Win and Retain Customers?
Safety & Security are Top of Mind
Safe Environment for Passengers and Staff
How to Reduce Interruptions and Delays?
Better Utilisation of Assets
Facilitate more train movements
How to Improve Reliability and Reduce Downtime?

## Slide 7: Agenda
The Opportunity for Further Progress
Coming: The Cost Avalanche
IP for Trackside Comms: Achieving Reliability
The Cisco Connected Signalling Architecture

## Slide 8: Railway Infrastructure Operators and Telecom Providers
Telecom Providers
Extensive fibre-optic networks
Need to provide very-high availability of services
Railway Infrastructure Operators
Nation-wide fibre-optic networks
Need to provide very-high availability of services
Some important similarities

## Slide 9: Railway Infrastructure Operators and Telecom Providers
Telecom Providers
Have migrated from ATM / TDM over SDH to higher capacity design of Ethernet and IP
Railway Infrastructure Operators
Beginning to explore the possibilities of new network technologies
And one major difference

## Slide 10: Railway Infrastructure Operators and Telecom Providers
The Facts:
100% of the world’s 25 largest telecom providers have migrated to Ethernet and IP
Most telecom providers will stop investments in SDH by 2010 at the latest
By focussing on IP, 69% of telecom providers expect savings from 11% to over 50%
Why telecom providers have migrated to IP
Source: Infonetics Research, Service Provider Plans for Packet Optical Transport and 40G, Oct 2008

## Slide 11: Railway Infrastructure Operators and Telecom Providers
What this means to you
Major Purchasers of SDH Depart
SDH Now Effectively at End-of-Life
Spare Parts, Skills Become Rare and Expensive

## Slide 12: Railway Infrastructure Operators and Telecom Providers
What this means to you
Major Purchasers of SDH Depart
SDH Now Effectively at End-of-Life
Spare Parts, Skills Become Rare and Expensive
How will you increase operational efficiency and still innovate and grow the business
?

## Slide 13: Agenda
The Opportunity for Further Progress
Coming: The Cost Avalanche
IP for Trackside Comms: Achieving Reliability
The Cisco Connected Signalling Architecture

## Slide 14: Is an IP Network Reliable Enough for Railway Telecoms?
Like my Internet at Home?
How will we deal with Hackers?
?
?
?
Signalling data behind ... ... a slow iTunes download?

## Slide 15: IP Networks for Signalling and Train Control
IP was developed for defence applications
Development of TCP/IP began in the early 1970’s, at the U.S. Defence Advanced Research Projects Agency (DARPA)
Main driver for this communications protocol was to control nuclear armaments under severe conditions
IP is a “connection-less” protocol; it is assumed that the physical network is unreliable and subject to failure

## Slide 16: CENELEC 50159-2 Railway Standard
Open Transmission Network (SIL 0)

## Slide 17: Achieving Survivability of the Network
Characteristics* | Applied to the IP Network
Hardness resistance to deformation | Robust, proven products with very high measured MTBF
Stealth ability to conceal itself | Network security to restrict access and counter intrusion
Redundancy duplication of critical system components | Redundant paths, devices, fans, power supplies
Diversity variation of systems; mitigation of fragility in changing conditions | Fast convergence to meet or exceed the performance of SDH; QoS to prioritize traffic under changing conditions
* From Defining Survivability for Engineering Systems, by M.G. Richards, D.H. Rhodes, D.E. Hastings and A.L. Weigel, MIT, March 2007.

## Slide 18: Some of the Measures used to Achieve Resilience
Mission-Critical Network Design
Redundancy: at Sites, in Components within the Devices, Redundant Links
Very High (measured) MTBF of Devices
Comprehensive Network Security Measures
Fast Network Convergence* (< 50ms)
* Ability of the network components to adapt to changes in topology, routing paths
Notes: Survivability: The ability of a system to minimize the impact of a finite disturbance on value delivery achieved through either
  the satisfaction of a minimally acceptable level of value delivery during and after a finite disturbance or
  the reduction of the likelihood or magnitude of a disturbance
Resilience: The ability of a network to continue to provide and maintain an acceptable level of service in the face of faults and challenges to normal operation
Service-Level Definitions are a key design consideration!

## Slide 19: Agenda
The Opportunity for Further Progress
Coming: The Cost Avalanche
IP for Trackside Comms: Achieving Reliability
The Cisco Connected Signalling Architecture

## Slide 20: Architectural Approach to Addressing Business Needs
All components EN 50121-4 compliant

## Slide 21: Network Topology
Access Layer
Mission Critical Services

## Slide 22: Network Topology
Access Layer
Standard Services

## Slide 23: Network Topology
Standard Services
Access Layer
Mission Critical Services

## Slide 24: Network Topology
Mission Critical Services
Standard Services
Access Layer
Distribution

## Slide 25: Network Topology
DWDM Infrastructure
Access
Distribution
Core

## Slide 26: Some Examples
Cisco IP MPLS network: delivers line side voice, monitoring and, soon, GSM-R backhaul at Rail Net Denmark
Cisco IP MPLS network: IP CCTV from 400 stations into centralised security operations and archives
Cisco IP MPLS network: Long Line PA into more than 250 stations
Cisco IP MPLS network: GSM-R backhaul

## Slide 27: Summary
Our Recommendations:
Avoid the “cost avalanche” associated with SDH – Act Now
An IP MPLS Multi-Service Network adheres to your standards, supports better utilisation of your assets
Design and build your telecoms network for future needs